## Slide 1
CAFE Baseline dissemination workshop
27/09/2004
Dr. Leonidas Mantzos
E3M-LAB/ICCS NTUA
contact: Kapros@central.ntua.gr
Energy projections as input to the CAFE baseline
PRIMES projections and national perspectives

## Slide 2: CAFE Energy Baseline scenario PRIMES projections
Starting point: LREM baseline scenario (developed for DG-TREN)
  Finalised in December 2002
  Climate policies measures not included explicitly
CAFE baseline scenario incorporates:
  Climate policy measures
    The existence of an EU-wide emissions trading regime is assumed
    The permit price ranges from 12 €00 per t of CO2 in 2010 to 16 €00 in 2015 and 20 €00 in 2020-2030 leading to adjustment of the behaviour of economic agents through changes in relative fuel prices
  Member States comments
    It maintains however a Europe-wide consistency in assumptions about energy prices, imports and exports of electricity etc.
  Revised macroeconomic assumptions reflecting latest trends
  Latest data as regards the evolution of the EU-25 power generation sector

## Slide 3: The EU-25 energy system in the horizon to 2020
EU-25 population remains rather stable to 2000 levels
GDP grows at a rate of 2.3% pa in 2000-2020
  2.0% pa in 2000-2010
Primary energy needs reach at 1.8 Gtoe in 2020 (from 1.65 in 2000)
Energy imports rise by 1.8% pa
Electricity production grows by 1.4% pa
  25000 MW of new power plants per year (for expansion and replacement)
CO2 emissions in 2020 are slightly below 2000 levels
    -7.4% from 1990 levels in 2010, -3.6% in 2020
    Key role for New Member States
      In EU-15 CO2 emissions reach at -3.6% from 1990 levels in 2010 and +0.6% in 2020 (from +1.2% in 2000)
      In NMS they reach at -24.8% in 2010 and -22.5% in 2020 (from -20.4% in 2000)

## Slide 4: EU-25 primary energy needs: Structure by fuel
Natural Gas: strategic importance, close to 160% of incremental demand
Renewables: high growth but still have a low share (10% in 2020)
Oil: sector-specific fuel, stable demand but maintains high share in consumption
Nuclear: decreases after 2010, depends on plants’ lifetime and nuclear phase-out policies
Solids: continuous decline in the horizon to 2020

## Slide 5: EU-25: CO2 emissions
The Transport sector is mainly responsible for increased emissions and the persisting dependence on oil imports
The Electricity Generation sector (part of Supply Side) is responsible for higher CO2 emissions in the long run, as part of nuclear is decommissioned

## Slide 6: EU-25: Demand side
The bulk of additional energy needs in the demand side come from transport activity
Electricity needs continuously rise while natural gas also gains additional market share over the projection periods.
By 2030, CO2 emissions in the transport sector account for close to 50% of total CO2 emissions in the demand side

## Slide 7: EU-25: Power generation sector
Gas is key for power generation market expansion in the horizon to 2020
Renewable energy forms also grow significantly with their market share in electricity generation reaching 20.2% in 2010 and 22.4% in 2020

## Slide 8: EU-25: Investment in Power Generation
In 15 years, 620 GW of new Power Investment (funds up to 550 billion €) need to be constructed
  355 GW Gas-fired, 36 GW Advanced Coal, 180 GW Renewables and 12 GW Nuclear
a big challenge for the liberalized market

## Slide 9: Comparison to the LREM Baseline scenario
Climate policy measures have a key role in the projected evolution of the EU-25 energy system under CAFÉ baseline scenario assumptions
Lower economic growth results in less pronounced energy intensity gains but also a more favourable development for carbon intensity

## Slide 10: Concluding remarks
Sustained economic growth can take place with low additional energy needs: considerable energy efficiency gains, as economic growth is driven by less energy intensive sectors
Electricity is essential for consumer’s welfare, electricity generation and supply is also essential for energy policy.
Transportation is also crucial for welfare: challenges for policy to deliver technological change, fuel efficiency and environmental improvement
Energy Imports grow four times faster than total energy needs, raising security of supply concerns (import dependency close to 62% in 2020)
Evidence of saturation effects as regards the further decarbonisation of the energy system beyond 2010 even in the presence of climate policy measures